## Slide 1
Quality of the MODIS and VIIRS ocean color time series following the R2022 reprocessing
MODIS/VIIRS Science Team Meeting
2-4 May 2023
College Park, MD
Bryan Franz
Ocean Ecology Laboratory
NASA Goddard Space Flight Center

## Slide 2
NASA Ocean Biology Processing Group & OB.DAAC
Global Processing & Distribution
VIIRS/JPSS2 (USA)
VIIRS/JPSS1 (USA)
VIIRS/SNPP (USA)
MODIS/Aqua (USA)
MODIS/Terra (USA)
OLCI/S3A (Europe)
OLCI/S3B (Europe)
SeaWiFS (USA)
MERIS (Europe)
OCTS (Japan)
CZCS (USA)
Regional Processing & Distribution
Hawkeye (USA)
GOCI (South Korea)
HICO (USA)
calibration, validation, software development, (re)processing, and distribution for a multitude sensors
Phytoplankton Chlorophyll
Particulate Backscatter
JPSS-2 VIIRS Ocean Color Products Now Available!
15-22 April 2023
15-22 April 2023

## Slide 3: R2022 Multi-mission Ocean Color Reprocessing
Missions:
  VIIRS (SNPP, J1, J2), MODIS (Aqua, Terra), OLCI (S3A, S3B), SeaWiFS, MERIS, OCTS, CZCS
Changes:
instrument and vicarious calibration updates
updates to ancillary data sources
  from NCEP/TOMS-OMI/etc. to MERRA-2 assimilation product
updates to atmospheric correction methods and tables
  multi-scattering aerosol selection, extended AOT range, improved/expanded absorbing gas corrections, Rayleigh hi-solz bug
updates to pure seawater optical properties (nw, aw, bbw)
  apply temperature & salinity dependence (e.g., Werdell et al. 2013), bug in pure-water aw/bbw (off by few nm)
updates to masks and flags
  reduced straylight flagging/masking (Hu et al. 2019, JGRO), absorbing aerosol flag based on MERRA-2 transport model
updates to derived product algorithms
  Chl coefficient update (Hu et al. 2019, JGRO; O'Reilly and Werdell, 2019), PIC, PAR, etc.

## Slide 4: Seasonal Mean Chlorophyll Concentration for 2022
MODIS
VIIRS
Aqua
Terra
JPSS-1
SNPP
Boreal Fall 2022
Boreal Fall 2022
Boreal Fall 2022
Boreal Fall 2022

## Slide 5: R2018 Global Deep-Water Chlorophyll Trends
VIIRS/JPSS1 & VIIRS/SNPP
MODIS/Aqua & MODIS/Terra
VIIRS/SNPP & MODIS/Aqua
MODIS/Terra & SeaWiFS
Chl (mg m-3)
Chl (mg m-3)
Chl (mg m-3)
Chl (mg m-3)
VIIRS/SNPP
MODIS/Aqua
VIIRS/SNPP
VIIRS/JPSS1
Comparison trends over common mission lifetime
VIIRS/SNPP shows negative trend relative to VIIRS/JPSS1 & MODIS/Aqua
SeaWiFS, MODIS/Terra, MODIS/Aqua in good agreement, with short-term deviations

## Slide 6: R2022 Global Deep-Water Chlorophyll Trends
VIIRS/JPSS1 & VIIRS/SNPP
MODIS/Aqua & MODIS/Terra
VIIRS/SNPP & MODIS/Aqua
MODIS/Terra & SeaWiFS
Chl (mg m-3)
Chl (mg m-3)
Chl (mg m-3)
Chl (mg m-3)
VIIRS/SNPP
MODIS/Aqua
VIIRS/SNPP
VIIRS/JPSS1
Comparison trends over common mission lifetime
VIIRS/SNPP now in good agreement with VIIRS/JPSS1 & MODIS/Aqua
SeaWiFS, MODIS/Terra, MODIS/Aqua still in good agreement, with short-term deviations

## Slide 7: R2022 Deep-water Rrs, MODIS/Aqua & SNPP/VIIRS +Northern & Southern Hemisphere Temperate Zone
Rrs (sr-1)
Rrs (sr-1)
Rrs (sr-1)
NH
SH
MODIS/Aqua & VIIRS/SNPP in very good agreement!
Deviation in blue prior to 2016 likely residual error from tungsten oxide contamination on VIIRS mirror
Deviation in blue post 2020 in SH are TBD (MODIS issue)

## Slide 8: R2022 Deep-water Rrs, SNPP/VIIRS & J1/VIIRS +Northern & Southern Hemisphere Temperate Zone
Rrs (sr-1)
Rrs (sr-1)
Rrs (sr-1)
NH
SH
VIIRS/SNPP & J1 in exellent agreement
Artifact near Jan 2020 in SH is Australian fires

## Slide 9: R2022 Hemispherical Deep-water Chlorophyll Trends Northern & Southern Hemisphere Temperate Zone
Excellent agreement demonstrates that the consistently-processed VIIRS time-series can be used to extend the ocean color data record established with SeaWiFS and MODIS for many key parameters.
SH peak in Jan 2020 captures phytoplankton blooms generated by Australian fires.
Chl (mg m-3)
Chl (mg m-3)
MODIS/Aqua & VIIRS/SNPP
MODIS/Aqua & VIIRS/J1
NH
SH
NH
SH

## Slide 10: R2022 MODIS/Aqua Rrs Validation
Comparison against AERONET-OC and SeaBASS in situ measurements.
Very good agreement in most bands.
Negative mean relative bias of < 5% in most bands (Bland Altman).
Rrs (443) Scatter
Rrs (547) Scatter
Rrs (547) Freq. Dist.
Rrs (443) Freq. Dist.
Rrs (443) Bland Altman
Rrs (547) Bland Altman
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 11: R2022 VIIRS/SNPP Rrs Validation
Comparison against AERONET-OC and SeaBASS in situ measurements.
Very good agreement in most bands.
Negative mean relative bias of < 5% in most bands (Bland Altman).
Rrs (443) Scatter
Rrs (551) Scatter
Rrs (551) Freq. Dist.
Rrs (443) Freq. Dist.
Rrs (443) Bland Altman
Rrs (551) Bland Altman
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 12: R2022 VIIRS/JPSS1 Rrs Validation
Comparison against AERONET-OC and SeaBASS in situ measurements.
Very good agreement in most bands.
Negative mean relative bias of < 5% in most bands (Bland Altman).
Rrs (445) Scatter
Rrs (556) Scatter
Rrs (556) Freq. Dist.
Rrs (445) Freq. Dist.
Rrs (445) Bland Altman
Rrs (556) Bland Altman
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 13: Anomalous results observed in 2022
Chl (mg m-3)
Cphyto (mg m-3)
2022 Seasonal Cycle and SeaWiFS-MODISA Climatology
SeaWiFS-MODISA Time-Series and
De-seasonalized Anomalies
Chl (mg m-3)
Cphyto (mg m-3)
NH
NH
SH
SH
EQ
EQ
B.A. Franz, I. Cetinic, M. Gao, D.A. Siegel, and T.K. Westberry (2023). Global ocean phytoplankton [in State of the Climate in 2022]. BAMS, in review.

## Slide 14: Impact of 2022 Hunga Tonga Eruption
NH
SH
OMPS Stratospheric Aerosol
All ocean color missions showing large deviation in Rrs through 2022, largest % diff in green-red.
Issue believed to be atmospheric correction error due to unmodeled stratospheric aerosols.
Operating assumption is that ocean reflectance (Rrs) is underestimated because the correction for ozone absorption does not account for scattering by high-altitude aerosols.
Rrs (green) Seasonal Cycles in South Pacific Gyre
MODIS/Aqua
MODIS/Terra
VIIRS/SNPP
VIIRS/JPSS1
OLCI/S3A
OLCI/S3B
B.A. Franz, A. Sayer, I. Cetinic, A. Ibrahim, manuscript in development

## Slide 15: Summary
JPSS-2 VIIRS ocean color products are now available through OB.DAAC.
R2022 ocean color reprocessing completed for all missions. VIIRS Rrs time series from SNPP and JPSS-1 in good agreement with MODIS, indicating that VIIRS can be used to extend the SeaWIFS-MODIS time series for many key OC parameters.
R2022 Rrs (and Chl) results are in good agreement with in situ measurements for all missions, with Rrs bias < 5% (typically negative) in all bands.
All ocean color missions are showing anomalous trends in Rrs through 2022 that appear to be due to atmospheric correction error associated with unresolved stratospheric aerosols from the Hunga Tonga eruptions of Jan 2022. Detailed analyses underway; mitigation strategy in development.

## Slide 16: MODIS-Aqua Daily Chlorophyll – R2018
Includes 5 X 7 STRAYLIGHT masking of Level-2 pixels around bright targets

## Slide 17: MODIS-Aqua Daily Chlorophyll – R2022
Includes 3 X 3 STRAYLIGHT masking of Level-2 pixels around bright targets

## Slide 18: Multi-Scattering Epsilon (MSEPS) Atmospheric Correction
TOA reflectance
Step 1
Rayleigh, gas, and glint correction
Step 2
Estimate the optical depth at the longest high radiometric quality band for each relative humidity aerosol model set
Step 3
From (multi-scattering) Epsilon, find the closest aerosol fine mode fractions (FMF).
Step 4
Calculate the spectral aerosol reflectance for the closest models in relative humidity and FMF space
Rrs ,𝝉a , Ångström
Step 5
Calculate the weighted mean of the models to get the final aerosol reflectance and diffuse transmittance
Ahmad, Z. and B. Franz (2018), Uncertainty in aerosol model characterization and its impact on ocean color retrievals, in PACE Technical Report Series, Volume 6: Data Product Requirements and Error Budgets (NASA/TM-2018 - 2018-219027/ Vol. 6).

## Slide 19: R2022 MODIS-Aqua Chl Validation
Chl Scatter
Chl Freq. Dist.
Chl Bland Altman
MODIS-Aqua Chlorophyll in good agreement with in situ measurements
Mean positive relative bias < 5%
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 20: R2022 VIIRS-SNPP Chl Validation
Chl Scatter
Chl Freq. Dist.
Chl Bland Altman
MODIS-Aqua Chlorophyll in good agreement with in situ measurements
Mean positive relative bias < 5%
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 21: Seasonal Mean Chlorophyll Concentration for 2022
MODIS
OLCI
Aqua
Terra
Boreal Fall 2022
Boreal Fall 2022
Boreal Fall 2022
Boreal Fall 2022
Sentinel-3A
Sentinel-3B

## Slide 22: OLCI-S3A vs MODIS-A, R2022 Global Deep-Water Trends
Oligotrophic
Mesotrophic
Eutrophic
Rrs (sr-1)
Chl (mg m-3)

## Slide 23: OLCI-S3B vs MODIS-A, R2022 Global Deep-Water Trends
Oligotrophic
Mesotrophic
Eutrophic
Rrs (sr-1)
Chl (mg m-3)

## Slide 24: R2022 OLCI/S3A Rrs Validation
Comparison against AERONET-OC and SeaBASS in situ measurements.
Very good agreement in most bands.
Negative mean relative bias of < 5% in most bands (Bland Altman).
Rrs (443) Scatter
Rrs (560) Scatter
Rrs (560) Freq. Dist.
Rrs (443) Freq. Dist.
Rrs (443) Bland Altman
Rrs (560) Bland Altman
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 25: R2022 OLCI/S3B Rrs Validation
Comparison against AERONET-OC and SeaBASS in situ measurements.
Very good agreement in most bands.
Negative mean relative bias of < 5% in most bands (Bland Altman).
Rrs (443) Scatter
Rrs (560) Scatter
Rrs (560) Freq. Dist.
Rrs (443) Freq. Dist.
Rrs (443) Bland Altman
Rrs (560) Bland Altman
https://seabass.gsfc.nasa.gov/search_results/val

## Slide 26: Monthly Mean SST for March 2023
MODIS
VIIRS
Aqua
Terra
SNPP
March 2023
March 2023
March 2023
JPSS-1 VIIRS coming soon.