## Slide 1: Seasonally varying bias in MODIS/Aqua ocean color retrievals and its potential relationship to polarization sensitivity
Amir Ibrahim and Gerhard Meister
NASA
MODIS/VIIRS Science Team Meeting
May 2nd, 2024

## Slide 2: Outline
Background on the seasonal bias
Investigating bias in SeaWiFS, MODIS Aqua, Terra, and SNPP
SeaBASS validation at MOBY
Conclusion

## Slide 3: Elements with potential impact on seasonal bias
Instrument calibration (cross-calibration, polarization correction, RVS, trends, etc.)
MOBY timeseries data (calibration issues, BRDF correction, vertical depth Lu extrapolation, surface effects).
Vicarious calibration procedure (i.e., absolute calibration at NIR, data filtering, spatial variability).
Atmospheric correction (BRDF correction, glint, aerosol type).
Uncertainties in both in-situ as well as satellite retrievals.

## Slide 4: Background
Much of this work stemmed from a comparative analysis by K. Bisson between the backscattering coefficient derived from MODIS Aqua, CALIOP and Argo floats.
It was discovered that there is a seasonal and latitudinal discrepancy between MODIS and CALIOP and Argo floats.
This work summarized in the GRL paper.

## Slide 6: Global comparison

## Slide 7: Bias in the remote sensing reflectance (Rrs) Analysis at MOBY
MOBY
Satellite

## Slide 8: Bias in the remote sensing reflectance (Rrs) Analysis at MOBY
bias in the summer
Ratio to MOBY

## Slide 9: Multiple linear regression
Ideally all independent
variables will have a slope of 0 and Rrs_moby of 1
Potential contributors to the bias:
BRDF
The aerosol type and optical depth

## Slide 10: Study summary
Ocean color data are seasonally biased in low biomass regions.
In terms of IOPs, bbp is the most affected as it’s directly related to the magnitude of Rrs, while aph and adg are not.
The bias in Rrs is more pronounced towards longer wavelengths.

## Slide 11: Standard processing: 2018 vs 2022 SeaWiFS
small seasonal bias

## Slide 12: Standard processing: 2018 vs 2022 SNPP
some seasonal bias

## Slide 13: Standard processing: 2018 vs 2022 MODIS Aqua
Strong seasonal bias
Improvement in R2022

## Slide 14: Standard processing: 2018 vs 2022 MODIS Terra
Small seasonal bias

## Slide 15: POLYMER algorithm versus OBPG: MODIS Aqua
Ratio of Rrs POLYMER or OBPG and Rrs MOBY
Results from Robert Frouin
No SVC applied
Strong seasonal bias in the blue

## Slide 16: A further assessment of calibration
All sensors use the same algorithms for data processing but exhibit different seasonal biases.
The primary differences between sensors are related to their cross-calibration and polarization correction.
Cross-calibration aims to improve the Response versus scan calibration and estimate the polarization sensitivity.
Cross-calibration is performed differently for each sensor:
  SeaWiFS - no cross-calibration
  MODIS Aqua - cross-calibrated to itself
  MODIS Terra - cross-calibrated to Aqua
  VIIRS - no cross-calibration
The polarization correction for Terra is derived from Aqua, but Aqua utilizes pre-launch polarization characterization.
We are investigating cross-calibration of Aqua to SeaWiFS to derive new polarization elements m12 and m13.

## Slide 17: Polarization sensitivity impact on ocean color
The measured at-sensor radiance is the summation of unpolarized radiance* and the polarized radiance and modulated by the Mueller elements of the instrument.
If the the TOA radiance is unpolarized (i.e., and are zeros) or if the instrument has no sensitivity to the polarization (i.e., and are zeros), then = .
TOA radiance is highly polarized and with a polarization sensitive instrument,
The polarization sensitivity is defined as follows:
To perform correction, we need knowledge of:
  The polarized at-sensor radiance and (if not measured then approximated from Rayleigh scattering)
  and (pre-launch characterization of sensorss)
+
Polarized radiance unknown
Approximate the polarized radiance from Rayleigh model
*is the radiance that would be measured by a sensor with no polarization sensitivity
More details in Meister et al., 2005

## Slide 18: Polarization sensitivity xcal derived vs pre-launch
For ms1 and -20 scan angle

## Slide 19: Cross-calibration of Aqua to SeaWiFS (M11, m12, and m13)
LUT version axc61e

## Slide 20: Cross-calibration of Aqua to SeaWiFS, M11 Aqua xcal to Aqua
LUT version V2.7e

## Slide 21: Conclusion
OBPG is actively working on a resolution, as additional insight is needed.
The multispectral treatment of MOBY data introduces a constant bias in the validation process compared to SVC, which considers the full RSR of the satellite. Therefore, the validation process is being re-evaluated.
This constant bias exacerbates the impact of the seasonal bias magnitude.
Aqua shows significantly larger biases than SeaWiFS, Terra, and SNPP, suggesting an instrument-dependent issue (calibration) with Aqua.
While there may be residual algorithm biases (AC, BRDF, PS correction, etc.), they are likely not the primary cause of the seasonal bias in Aqua.
Cross-cal derived polarization sensitivity shows some improvement in reducing the seasonal bias. RVS has a strong impact in the blue and will be further investigated.

## Slide 22: Appendix

## Slide 23: Seasonal Bias at AERONET-OC sites

## Slide 24: Impact of glint

## Slide 25: Impact of glint

## Slide 26: Standard processing: 2018 vs 2022 MODIS Aqua
Seasonal bias exists
Improvement in R2022

## Slide 27: Impact of LUTs generated by PW Zhai RT code

## Slide 28: Cross-calibration of Aqua to SeaWiFs but with a normalized M11